## Slide 1: Addressing Modes

## Slide 2: Addressing Modes
immediate operand
  mov ax, 5
  Every reasonable program needs some data in memory apart from constants
  Constants cannot be changed, i.e. they cannot appear as the destination operand
  there must be a mechanism in assembly language to store and retrieve data from memory.

## Slide 3: . DATA DECLARATION
“define byte” written as “db.”
“define word” or “dw”
We can associate a symbol with any address that we want to remember and use that symbol in the rest of the code

## Slide 4: DIRECT ADDRESSING(ex2)
; a program to add three numbers using memory variables
[org 0x0100]
  mov ax, [num1] ; load first number in ax
  mov bx, [num2] ; load second number in bx
  add ax, bx ; accumulate sum in ax
  mov bx, [num3] ; load third number in bx
  add ax, bx ; accumulate sum in ax
  mov [num4], ax ; store sum in num4
  mov ax, 0x4c00 ; terminate program
int 0x21
num1: dw 5
num2: dw 10
num3: dw 15
num4: dw 0

## Slide 5: DIRECT ADDRESSING(ex3)
a program to add three numbers accessed using a single label
[org 0x0100]
  mov ax, [num1] ; load first number in ax
  mov bx, [num1+2] ; load second number in bx
  add ax, bx ; accumulate sum in ax
  mov bx, [num1+4] ; load third number in bx
  add ax, bx ; accumulate sum in ax
  mov [num1+6], ax ; store sum at num1+6
  mov ax, 0x4c00 ; terminate program
int 0x21
num1: dw 5
    dw 10
    dw 15
    dw 0

## Slide 6: DIRECT ADDRESSING(ex4)
; a program to add three numbers accessed using a single label
[org 0x0100]
  mov ax, [num1] ; load first number in ax
  mov bx, [num1+2] ; load second number in bx
  add ax, bx ; accumulate sum in ax
  mov bx, [num1+4] ; load third number in bx
  add ax, bx ; accumulate sum in ax
  mov [num1+6], ax ; store sum at num1+6
  mov ax, 0x4c00 ; terminate program
int 0x21
num1: dw 5, 10, 15, 0

## Slide 7: DIRECT ADDRESSING(ex5)
; a program to add three numbers directly in memory
[org 0x0100]
  mov ax, [num1] ; load first number in ax
  mov [num1+6], ax ; store first number in result
  mov ax, [num1+2] ; load second number in ax
  add [num1+6], ax ; add second number to result
  mov ax, [num1+4] ; load third number in ax
  add [num1+6], ax ; add third number to result
mov ax, 0x4c00 ; terminate program
int 0x21
num1: dw 5, 10, 15, 0
Notes: directly add a memory variable and a register instead of adding a register into another

## Slide 8: ERRORS
mov [num1+6], [num1] ; ILLEGAL
“mov ax, bl”
“mov [num1], [num2]

## Slide 9: Add three numbers using byte variables(ex6)
If we change the directive in the last example from DW to DB, the program will still assemble and debug without errors, however the results will not be the same as expected?
; a program to add three numbers using byte variables
[org 0x0100] mov al, [num1] ; load first number in al
  mov bl, [num1+1] ; load second number in bl
  add al, bl ; accumulate sum in al
  mov bl, [num1+2] ; load third number in bl
  add al, bl ; accumulate sum in al
  mov [num1+3], al ; store sum at num1+3
mov ax, 0x4c00 ; terminate program
int 0x21
num1: db 5, 10, 15, 0

## Slide 10: SIZE MISMATCH ERRORS
The instruction “mov [num1], 5” is legal but there is no way for the processor to know the data movement size in this operation.
mov byte [num1], 5
mov word [num1], 5
The programmer is responsible for accessing the data as word if it was declared as a word and accessing it as a byte if it was declared as a byte

## Slide 11: REGISTER INDIRECT ADDRESSING(ex7)
; a program to add three numbers using indirect addressing
[org 0x100]
  mov bx, num1 ; point bx to first number
  mov ax, [bx] ; load first number in ax
  add bx, 2 ; advance bx to second number
  add ax, [bx] ; add second number to ax
  add bx, 2 ; advance bx to third number
  add ax, [bx] ; add third number to ax
  add bx, 2 ; advance bx to result
  mov [bx], ax ; store sum at num1+6
mov ax, 0x4c00 ; terminate program
int 0x21
num1: dw 5, 10, 15, 0

## Slide 12: REGISTER INDIRECT ADDRESSING(ex8)
; a program to add ten numbers
[org 0x0100]
  mov bx, num1 ; point bx to first number
  mov cx, 10 ; load count of numbers in cx
  mov ax, 0 ; initialize sum to zero
  l1: add ax, [bx] ; add number to ax
  add bx, 2 ; advance bx to next number
  sub cx, 1 ; numbers to be added reduced
  jnz l1 ; if numbers remain add next
  mov [total], ax ; write back sum in memory
mov ax, 0x4c00 ; terminate program
int 0x21
num1: dw 10, 20, 30, 40, 50, 10, 20, 30, 40, 50
total: dw 0

## Slide 13: REGISTER + OFFSET ADDRESSING
; a program to add ten numbers using register + offset addressing
[org 0x0100]
  mov bx, 0 ; initialize array index to zero
  mov cx, 10 ; load count of numbers in cx
  mov ax, 0 ; initialize sum to zero
  l1: add ax, [num1+bx] ; add number to ax
  add bx, 2 ; advance bx to next index
  sub cx, 1 ; numbers to be added reduced
  jnz l1 ; if numbers remain add next
  mov [total], ax ; write back sum in memory
mov ax, 0x4c00 ; terminate program
int 0x21
num1: dw 10, 20, 30, 40, 50, 10, 20, 30, 40, 50 total: dw 0

## Slide 14: Class Activity(SEGMENT ASSOCIATION and ADDRESS WRAPAROUND)
For example if BX=0100, SI=0200, and CS=1000 and the memory access under consideration is [cs:bx+si+0x0700], what would be the effective address?
BX=9100, DS=1500 and the access is [bx+0x7000], is there is wraparound?
Notes: bx+si+0700 = 0100 + 0200 + 0700 = 0A00. Now multiplying the segment value by 16 makes it 10000 and adding the effective address 00A00 forms the physical address 10A00.

## Slide 15: Segment Override Prefix
Instruction opcode
Mov ax ,[cs:bx] 2E8B07
Mov ax ,[es:bx] 268B07
Mov ax ,[ss:bx] 368B07
Mov ax, [bx] 8B07