## Slide 1: Addressing Modes Summary

## Slide 2: Addressing Modes Summary
Operands can be
  Immediate
    e.g. ADD AX, 5
  Register
    ADD AX, BX
  Memory
    ADD [num1], AX

## Slide 3: Addressing Modes Summary (contd.)
Direct Addressing
  mov ax, [num1]
Based Register Indirect
  Mov [bp], ax
  Mov ax, [bx]

## Slide 4: Addressing Modes Summary (contd.)
Indexed Register Indirect
  Mov [si], ax
  Mov ax, [di]
Based Register Indirect + Offset
  Mov [bx+300], ax
  Mov ax, [bp+300]
  Mov ax,[bx+num1]

## Slide 5: Addressing Modes Summary (contd.)
Indexed Register Indirect + Offset
  Mov [si+300], ax
  Mov ax, [di+300]
  Mov [si+num1], ax
Base + Index
  Mov [bx+si] , ax
  Mov ax, [bp+di]

## Slide 6: Addressing Modes Summary (contd.)
Base + Index + Offest
  Mov [bx+si+300] , ax
  Mov [bx+si+num1] , ax

## Slide 7: Addressing Modes
Mov ax,[num1]
Mov ax,[bx]
Mov ax,[si]
Mov ax,[bx+num1]
Mov ax,[si+num1]
Mov ax,[bx+si]
Mov ax,[bx+si+num1]

## Slide 8: Offset Addressing
Default Segment=ds
Mov ax,[0x1234]
Mov ah,[0x1234]
Mov byte[0x1234],10
Mov word[0x1234],10

## Slide 9: Base Addressing
Default Segment=ds
Mov ax,[bx]
Mov byte[bx],10
Mov word[bx],10
Default segment =ss
Mov ax,[bp]
Mov byte[bp],10
Mov word[bp],10

## Slide 10: Base+Offset addressing
Default segment=ss
  Mov byte[bp+0x10]=10
  Mov word[bp+0x10]=10
Default segment=ds
  Mov ax,[bx+0x100]
  Mov byte[bx+0x100],10
  Mov word[bx+0x100],10

## Slide 11: Index+offset addressing
Default segment=ds
  Mov ax,[si+0x0100]
  Mov ax,[di+0x0100]
  Mov byte[si+0x0100],10
  Mov word[si+0x0100],10
  Mov byte[di+0x100],10
  Mov word[di+0x100],10

## Slide 12: Index addressing
Default segment=ds
  Mov ax,[si]
  Mov ax,[di]
  Mov byte[si],10
  Mov word[di],10

## Slide 13: Base+index addressing
Default segment=ds
  Mov ax,[bx+si]
  Mov byte[bx+si],10
  Move word[bx+di],10
Default segment=ss
  Mov word[bp+si],10
  Mov byte[bp+di],10

## Slide 14: Base +Index +Offset addressing
Default segment=ds
  Mov ax,[bx+si+0x100]
  Mov byte[bx+si+0x100],10
  Mov word[bx+si+0x100],10
Default segment=ss
  Mov byte[bp+si+0x100],10
  Mov word[bp+si+0x100],10

## Slide 15: Common Mistakes
Address is 16-bit long, contained in 16-bit Register
Mov al,[bl] Not allowed
Mov ax,[bx-si]
[BX+SI] is allowed, [BX-SI] is NOT allowed
[Base+Base], [Index+Index] both NOT allowed, [Base+Index] is allowed